Simulation 4
ME – 565
Spring, 2024

By: Andres F. Hoyos

Consider a vehicle with the following parameters:

W = 3000 lbs,
W_s = 2700 lbs,
x_1 = 3.5 ft,
x_2 = -4.5 ft,
h = -1.0 ft,
t = 6.0 ft,
I_z = 40000 lbs*ft^2,
I_x = 15000 lbs*ft^2,
c = 0.5 ft,
{partial L} over {partial %phi}_f = 40000 lbs*ft,
{partial L} over {partial %phi}_r = 5000 lbs*ft,
{partial L} over {partial dot %phi}_f = 1000 lbs*ft/sec,
{partial L} over {partial dot %phi}_f = 500 lbs*ft/sec,
p = d = 12 in,
%eta = 15:1 ,
%epsilon = 1 (steering gearbox efficiency, NOT roll steer coefficient – let’s call it 1),
K_s = 10 in*lbs/deg, and
t_m = 3 in.

Cornering coefficients:
For the linear part of the simulation use: C_i = 140 lbs/deg.

The following formula for nonlinear tire stiffness can be used where W is the weight on a given tire in pounds (lbs):

C_i = (0.2*W_i - 0.0000942*W_i^2) lbs/deg.

Initial setup:

Before proceeding with the simulation, an initial set up is required. The first step will be to convert units since some units are incompatible. Note: ft are going to be used instead of in.

Unit conversions:

1. I_z = {I_z} over {g} = {40000} over {32.174} = 1243.2 lb*ft → lbm*ft.

2. I_x = {I_x} over {g} = {15000} over {32.174} = 466.215 lb*ft → lbm*ft.

3. p = p over 12 = 12 over 12 = 1 in → ft.

4. d = d over 12 = 12 over 12 = 1 in → ft.

5. K_s = (K_s)(1 over 12)(180 over %pi) in*lbs/deg → in*lbs/rad

6. t_m = t_m over 12 = 3 over 12 in → ft.

Some necessary calculations:

Masses can be computed as

m = W over g = 93.243 lbm,

m_s = W_s over g = 83.919 lbm.

The cornering stiffnesses of each axle can be calculated from the given information. The cornering stiffnesses are for the tires, hence, to get the cornering stiffness of the axle, the left and right tire cornering stiffnesses for that axle should be added and the units can be converted to compatible ones with the notation used on this work:

C_1 = (C_1r + C_1l)(180 over %pi) = (140+140)(180 over %pi) = 16043 lbs/rad,

C_2 = (C_2r + C_2l)(180 over %pi) = (140+140)(180 over %pi) = 16043 lbs/rad.

The following Matlab script loads the parameters into the workspace and performs all the calculations previously mentioned (Note: this code snippet should be executed before running the next scripts for part 1):

%% Load some initial values:
% Conversion factors:
deg2rad = pi / 180;
rad2deg = 180 / pi;
in2ft = 1 / 12;
ft2in = 12;
mph2ftps = 5280 / 3600;
ftps2mph = 3600 / 5280;
% Bicycle model parameters:
W = 3000; % lbs
Ws = 2700; % lbs
g = 32.174; % ft/sec^2
x1 = 3.5; % ft
x2 = -4.5; % ft = -1.0; % ft
h = -1.0; % ft
track_width = 6.0; % ft
Iz = 40000 / g; % lbs*ft^2
Ix = 15000 / g; % lbs*ft^2
c = 0.5; % ft
dl_phi_f = 8000; % lbs*ft
dl_phi_r = 5000; % lbs*ft
dl_dphi_f = 1000; % lbs*ft
dl_dphi_r = 500; % lbs*ft
p = 12*in2ft; % ft
d = 12*in2ft; % ft
gear_ratio = 15; % []
efficiency = 1.0; % Steering gearbox efficiency
Ks = 10*in2ft*rad2deg; % (in*lbs/deg)*(ft/in)*(deg/rad) -> ft*lbs / rad
tm = 3*in2ft; % in*(ft/in)-> ft - Pneumatic trail
% Masses:
m = W / g;
ms = Ws / g;
% u = 30; % ft/sec
C1 = 2*140*180/pi; %*rad2deg; % lbs/deg * (deg/rad) -> lbs / rad
C2 = 2*140*180/pi; % *rad2deg; % lbs/deg * (deg/rad) -> lbs / rad
l2 = x1 - x2; % Wheelbase
dt = 0.01;
t_initial = 0;
t_final = 5;

Part 1: 2-DoF Vehicle (Linear + Non-Linear)

1. Develop a base 2-DoF linear state space yaw rate model and calculate the system eigen values
when forward speed is 30 and 60 mph.

The 2-DoF Yaw Plane Model in state space form is given by

left [matrix{dot %beta ## dot r} right] = left [ matrix { {-C_1 - C_2} over {mu} # {-x_1 C_1 - x_2 C_2} over {mu} - 1 ## {-x_1 C_1 - x_2 C_2} over {I_z} # {-x_1^2 C_1 - x_2^2 C_2} over {I_z u}} right ] cdot left [ matrix{%beta ## r} right] + left [ matrix{{C_1} over {mu} ## {x_1 C_1} over {I_z}} right] cdot left [ matrix{%delta} right] ,

where

A = left [ matrix { {-C_1 - C_2} over {mu} # {-x_1 C_1 - x_2 C_2} over {mu} - 1 ## {-x_1 C_1 - x_2 C_2} over {I_z} # {-x_1^2 C_1 - x_2^2 C_2} over {I_z u}} right ] and B = left [ matrix{{C_1} over {mu} ## {x_1 C_1} over {I_z}} right] .

The eigenvalues of A matrix are the pole locations of the system. Hence, the eigenvalues for u=30 mph and u=60 mph can be calculated from A matrix. To solve the problem, the following Matlab script was written:

%% 1. Develop a base 2-DoF linear state space yaw rate model and calculate the system eigen values
% when forward speed is 30 and 60 mph
u30 = 30*mph2ftps;
u60 = 60*mph2ftps;
A30 = [
(-C1 - C2)/(m*u30), (((-x1*C1 - x2*C2)/(m*u30^2)) - 1);
(-x1*C1 - x2*C2)/(Iz), (-x1*x1*C1 - x2*x2*C2)/(Iz*u30);
]
A60 = [
(-C1 - C2)/(m*u60), ((-x1*C1 - x2*C2)/(m*u60^2)) - 1;
(-x1*C1 - x2*C2)/(Iz), (-x1*x1*C1 - x2*x2*C2)/(Iz*u60);
]
eg_30mph = eig(A30)
eg_60mph = eig(A60)

Running this code generates the following results:

A30 =

   -7.8206 -0.9111
   12.9040 -9.5314

A60 =

   -3.9103 -0.9778
   12.9040 -4.7657

eg_30mph =

  -8.6760 + 3.3205i
  -8.6760 - 3.3205i

eg_60mph =

  -4.3380 + 3.5262i
  -4.3380 – 3.5262i

Analysis P1Q1: Given these results, it can be seen that the real part of the eigenvalues have been halved after increasing the speed from 30 mph to 60 mph. It can be seen that the system became slower after performing this change. Moreover, it can be seen that as the speed increased from 30 mph to 60 mph, the imaginary part increased in magnitude which means that the transient response at 60 mph is going to have more oscillations than the transient response at 30 mph since imaginary poles produce oscillatory behaviors.

2. Using the steady-state yaw rate response, construct plots from 0 to 120 mph (i.e. 10 by 10) for various speeds, every 10 mph or so.

The following code is written in Matlab to solve the exercise:

%% 2. Using the steady-state yaw rate response, construct plots from 0 to 120 mph (i.e. 𝑟/𝛿 ) for various
% speeds, every 10 mph or so.
speeds = linspace(10, 120, 12)*mph2ftps;
delta2r_gain_arr = zeros(1, length(speeds));
t = linspace(t_initial, t_final, (t_final - t_initial) / dt);
figure;
hold on;
grid on;
title('Yaw rate steady state gains for different speeds')
xlabel('Time (seconds)');
ylabel('Gain (𝑟/𝛿)');
xlim([0, 5]);
ylim([0, 10.0]);
K_understeer = -m*(x1*C1 + x2*C2)/(C1*C2*l2);
legend_arr = cell(1, length(speeds));
for i = 1:length(speeds)
u = speeds(i);
delta2r_gain_arr(i) = u / (l2 + u*u*K_understeer);
% plot each gain in an xy plot:
yline(delta2r_gain_arr(i),'--', ['s.s gain = ' num2str(delta2r_gain_arr(i)) ' @ ' num2str(u*ftps2mph) 'mph'], 'Color', rand(1,3), 'LineWidth', 2);
% plot(t, delta2r_gain_arr(i)*ones(length(t)), '--', 'LineWidth', 2);
legend_arr{i} = [num2str(u*ftps2mph) ' mph'];
hold on;
end
legend(legend_arr{:}, 'Location', 'eastoutside');
hold off;

Note: the code converts the speed units from mph to ft/sec and then converts back to mph to plot the results.

The code generates the following results:

Figure 1: Shows the steady state gains of this vehicle for different speeds.

Analysis P1Q2: It can be seen from Figure 1 that before 70 mph, the steady-state gain increases, but after this value, the steady state gain decreases. A more in depth analysis will be to actually calculate the characteristic speed that will give information on exactly at which speed does the yaw rate steady state gain starts decreasing. The characteristic speed can be calculated as follows

u_{char} = sqrt{{x_1 - x_2} over {K_understeer}} = sqrt{8 over {7.2652*10^{-4}}} = 104.94 ft/sec = 71.55 mph, where

K_understeer = {-m(x_1 C_1 + x_2 C_2)} over {C_1 C_2 l_2} = 7.2652*10^-4 .

This value is consistent with the experiment shown in Figure 1. Also, given that the understeering coefficient is positive, this means that the vehicle, given its configuration, has a tendency to understeer.

3. Using the 2-DoF equations of motion, simulate the vehicle response to a steering input.
Determine the steering input required to result in a 400 ft radius turn. (hint: knowing the forward speed and radius of a circle, the required yaw rate can be calculated). Repeat the result at increments of 10 mph from 10 to 120 mph. Compare the results with the steady-state results from 2) above. We are using this step to validate your model.

To result in a turn radius of 400 ft, the steady state gain from steering wheel angle to yaw rate and the centripetal acceleration equation can be used to determine the required steering wheel angle δ as follows

r_ss over %delta = (u/R) over {%delta} = u over {l_2 + u^2 K_understeer} ,

thus

%delta = {l_2 + u^2 K_understeer} over R .

The following code is written in Matlab to solve this exercise applying the formula just presented to calculate the steering input required to produce a 400 ft radius turn:

%% 3. Using the 2-DoF equations of motion, simulate the vehicle response to a steering input.
% Determine the steering input required to result in a 400 ft radius turn. (hint: knowing the forward
% speed and radius of a circle, the required yaw rate can be calculated). Repeat the result at
% increments of 10 mph from 10 to 120 mph. Compare the results with the steady-state results from
% 2) above. We are using this step to validate your model.
radius = 400; % ft
speeds = linspace(10, 120, 12);
speeds = speeds*mph2ftps;
% Time domain simulation:
t_initial = 0; % sec
t_final = 5; % sec
dt = 0.01; % sec
t = linspace(t_initial, t_final, (t_final - t_initial) / dt);
figure;
subplot(3,1,1);
title('Steady state gains at different speeds');
xlabel('Time (seconds)');
ylabel('Gain []');
hold on;
grid on;
subplot(3,1,2);
title('Yaw rate response at different speeds');
xlabel('Time (seconds)');
ylabel('Yaw rate (rad/sec)');
hold on;
subplot(3,1,3);
title('Steering angle input at different speeds');
xlabel('Time (seconds)');
ylabel('Steering angle (rad)');
hold on;
legend_gains_arr = cell(1, length(speeds));
legend_yaw_rate_arr = cell(1, length(speeds));
legend_steering_angle_arr = cell(1, length(speeds));
for i = 1:length(speeds)
u = speeds(i);
subplot(3,1,1);
yline(delta2r_gain_arr(i),'--', ['s.s gain = ' num2str(delta2r_gain_arr(i)) ' @ ' num2str(u*ftps2mph) 'mph'], 'Color', rand(1,3), 'LineWidth', 2);
% plot(t, delta2r_gain_arr(i)*ones(length(t)), '--', 'LineWidth', 2);
legend_gains_arr{i} = ['s.s gain = ' num2str(delta2r_gain_arr(i)) ' @ ' num2str(u*ftps2mph) 'mph'];
subplot(3,1,2);
delta2 = (1 / radius)*(l2 + (u*u*K_understeer))*ones(1, length(t));
states_arr2 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta2);
plot(t, states_arr2(2,:));
legend_yaw_rate_arr{i} = ['Calculated s.s gain @ ' num2str(u*ftps2mph) ' is ' num2str(states_arr2(2, length(t))/delta2(length(t)))];
subplot(3,1,3);
plot(t, delta2);
legend_steering_angle_arr{i} = ['𝛿 = ' num2str(delta2(1)) ' @ ' num2str(u*ftps2mph) 'mph'];
end
subplot(3,1,1);
legend(legend_gains_arr);
grid on;
subplot(3,1,2);
legend(legend_yaw_rate_arr);
grid on;
subplot(3,1,3);
legend(legend_steering_angle_arr);
grid on;
hold off;

function states_arr = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta)
% Bicycle model using attack angle conventions:
% Attack angle is the negative of the slip angle
% The sign is embedded in the x1 and x2 distances
A = [
(-C1 - C2)/(m*u), ((-x1*C1 - x2*C2)/(m*u^2)) - 1;
(-x1*C1 - x2*C2)/(Iz), (-(x1^2)*C1 - (x2^2)*C2)/(Iz*u);
];
B = [
(C1)/(m*u);
(x1*C1)/Iz;
];
% Discretize using Euler:
A_dis = eye(2) + dt * A;
B_dis = dt * B;
% Initial conditions:
states = [0; 0];
states_arr = zeros(2,length(t));
% simulation loop:
for i = 1:length(t)
states = A_dis * states + B_dis * delta(i);
states_arr(:, i) = states;
end
end

This code generates the following result:

Figure 2: shows in the top subplot the steady state gains from steering wheel angle to yaw rate at different speeds, the middle subplot shows the time response of the yaw rate given the steering angle input signal shown in the bottom plot.

Analysis P1Q3: This code generates the plot shown in Figure 2, this figure has 3 subplots. The top subplot shows the steady state gains from steering wheel angle to yaw rate for different speeds. The subplot in the middle shows the time response of the yaw rate given the steering input in the bottom subplot.

Notice that the steady state gain values of the middle subplot on Figure 2 match with the steady state gains (plotted as horizontal lines) in the top subplot, this is a method of verification for the mathematical model proposed to solve this exercise. The steady state gain from question 1 gives information on the steady state gain, and this value is confirmed by the gain at which the yaw rate stabilized given the specified inputs.

Also, notice that as the speed increases, the steering wheel input signal increases, this makes sense as taking a sharper turn at high speeds will require higher controller effort.

4. Determine a particular time series of handwheel inputs. We define this input as a 0° handwheel
input for 1 second, then a +45° handwheel input for 3 seconds, then a −45° handwheel input for 3
seconds, then back to 0° for 3 seconds. Practically we know that the maximum handwheel input a
driver can perform is 2 𝑟𝑒𝑣/𝑠𝑒𝑐, so modify the steering input so that the handwheel velocity is
consistent with this value with a 180° input amplitude. Plot the time history of the steering input .

The steering rate saturation in radians per second is:

sat = 2*2*%pi = 4 %pi rad/sec.

The following code is written in Matlab to solve this exercise:

%% 4. Determine a particular time series of handwheel inputs. We define this input as a 0° handwheel
% input for 1 second, then a +45° handwheel input for 3 seconds, then a −45° handwheel input for 3
% seconds, then back to 0° for 3 seconds. Practically we know that the maximum handwheel input a
% driver can perform is 2 𝑟𝑒𝑣/𝑠𝑒𝑐, so modify the steering input so that the handwheel velocity is
% consistent with this value with a 180° input amplitude. Plot the time history of the steering input 𝛿.
% Time array:
t_initial = 0;
t_final = 10;
t = linspace(t_initial, t_final, (t_final - t_initial)/dt);
% Generate the specified handwheel input:
delta = zeros(1, length(t));
% Input of 0° for 1 second:
delta(1, 1:1/dt) = 0;
% Input of +45° for 3 seconds:
delta(1, 1/dt:4/dt) = 0.707;
% Input of -45° for 3 seconds:
delta(1, 4/dt:7/dt) = -0.707;
% Input of 0° for 3 seconds:
delta(1, 7/dt:length(t)) = 0;
% Plot input:
figure;
plot(t, delta);
grid on;
title('Steering input with no rate saturation');
xlabel('time (sec)');
ylabel('delta (rad)');
% Modify the steering input:
slope = 2*(2*pi); % rad/sec
% Smooth step applied at 1 second:
left_bound = 0;
right_bound = 0.707;
at = 1; % /dt;
delta_mod = slope_it_down(t, dt, at, delta, left_bound, right_bound, sign(right_bound - left_bound)*slope);
% Smooth step applied at 4 seconds:
left_bound = 0.707;
right_bound = -0.707;
at = 4; % /dt;
delta_mod = slope_it_down(t, dt, at, delta_mod, left_bound, right_bound, sign(right_bound - left_bound)*slope);
% Smooth step applied at 7 seconds:
left_bound = -0.707;
right_bound = 0;
at = 7; % /dt;
delta_mod = slope_it_down(t, dt, at, delta_mod, left_bound, right_bound, sign(right_bound - left_bound)*slope);
% Plot input:
figure;
plot(t, delta);
hold on;
plot(t, delta_mod, 'r');
grid on;
title('Steering input with smoothed angle transitions');
xlabel('time (sec)');
ylabel('delta (rad)');
legend('Original input signal', 'Modified input signal');

function delta = slope_it_down(t, dt, at, delta, left_bound, right_bound, slope)
time_to_reach = (right_bound - left_bound) / slope; % time units
delta(1, at/dt:(at + time_to_reach)/dt) = left_bound + slope * (t(at/dt:(at + time_to_reach)/dt) - t(at/dt));
end

This codes generates the steering signal shown in Figure 3 .

Figure 3: Steering input signal with steering angle rate saturation of 2 rev/sec. The plot compares the original input with no rate saturation (blue) and the modified input signal with rate saturation (red).

Analysis P1Q4: From Figure 3 it can be see that the steering angle now transitions from angle to angle with a ramp steady state. Physically this makes more sense as a human driver is not able to command a steering wheel with step signals.

However, even though the transitions have been smoothed out, this input signal is quite aggressive as the wheel are being suddenly turned to 45 deg and then from 45 deg to -45 deg and then to 0 deg; this is a signal that can potentially induce high lateral forces given the amplitude and the rapid rate of change, specially when the input signals transitions from a ramp to a constant as it produces a jump in steering rate and steering angular acceleration.

5. Use the steering input calculated in 4) as an input to your simulation. Plot the time history of the state variables drift angle and yaw rate 𝑟 at 30 and 60 mph.

The following code is developed in Matlab to perform this simulation and generate the plots:

%% 5. Use the steering input calculated in 4) as an input to your simulation. Plot the time history of the
% state variables drift angle 𝛽 and yaw rate 𝑟 at 30 and 60 mph.
% Speeds of interest:
u30 = 30*mph2ftps;
u60 = 60*mph2ftps;
% Time domain simulation:
states_arr30 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u30, delta_mod);
states_arr60 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u60, delta_mod);
% Plot the states:
figure;
subplot(2,1,1);
plot(t, states_arr30(1,:));
xlabel('time (sec)');
ylabel('drift angle (rad)');
grid on;
% title('yaw rate for 30 mph');
hold on;
plot(t, states_arr60(1,:));
xlabel('time (sec)');
ylabel('drift angle (rad)');
title('Drift angle for 30 and 60 mph');;
legend('30 mph', '60 mph');
subplot(2,1,2);
plot(t, states_arr30(2,:));
xlabel('time (sec)');
ylabel('yaw rate (rad/sec)');
grid on;
hold on;
plot(t, states_arr60(2,:));
title('Yaw rate for 30 and 60 mph');
legend('30 mph', '60 mph');

function states_arr = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta)
% Bicycle model using attack angle conventions:
% Attack angle is the negative of the slip angle
% The sign is embedded in the x1 and x2 distances
A = [
(-C1 - C2)/(m*u), ((-x1*C1 - x2*C2)/(m*u^2)) - 1;
(-x1*C1 - x2*C2)/(Iz), (-(x1^2)*C1 - (x2^2)*C2)/(Iz*u);
];
B = [
(C1)/(m*u);
(x1*C1)/Iz;
];
% Discretize using Euler:
A_dis = eye(2) + dt * A;
B_dis = dt * B;
% Initial conditions:
states = [0; 0];
states_arr = zeros(2,length(t));
% simulation loop:
for i = 1:length(t)
states = A_dis * states + B_dis * delta(i);
states_arr(:, i) = states;
end
end

This code generates the plot shown in Figure 4.

Figure 4: Yaw rate and drift angle time plots for 30 and 60 mph longitudinal speeds.

Analysis P1Q5: From the results shown in Figure 4, it can be supported again the statement done in part 1 – question 2 that the yaw rate gain increases with speed for speeds less than approximately 71 mph given that this is the characteristic speed of this understeering vehicle. Also, notice how the overshoot of the yaw rate response is bigger, this makes sense as the imaginary parts of the eigenvalues have higher absolute values.

Finally, it can be seen that the drift angle response decreases when increasing the speed from 30 mph to 60 mph.

6. Add nonlinear tires and assume equal roll moment front and rear, 60/40 biased to the front, and 40/60 biased to the rear. Compare your biased results to the results of 3)-5) with linear tires.

The front and rear axle cornering stiffnesses can be calculated as follows

C_1 = 2(0.2W_1 - 0.0000942 W_1^2)(180 over %pi) and C_2 = 2(0.2W_2 - 0.0000942 W_2^2)(180 over %pi) .

The following code was written in Matlab to compare the non-linear tire configurations with the linear tire behavior.

Comparison with 3:

%% 6. Add nonlinear tires and assume equal roll moment front and rear, 60/40 biased to the front, and
% 40/60 biased to the rear. Compare your biased results to the results of 3)-5) with linear tires.
%% Compare with 3):
close all;
speeds = linspace(10, 120, 12);
speeds = speeds*mph2ftps;
% Time domain simulation:
t = linspace(t_initial, t_final, (t_final - t_initial) / dt);
figure(1); % 50-50 weight bias
hold on;
figure(2); % 60-40 weight bias
hold on;
figure(3);
hold on;
legends_50_50 = {};
legends_60_40 = {};
legends_40_60 = {};
for i = 1:length(speeds)
u = speeds(i);
delta2 = (1 / radius)*(l2 + (u*u*K_understeer))*ones(1, length(t)); % (u / radius)*ones(1, length(t)); % Update delta to accomplish 400 ft radius
% Linear tire:
C1 = 2*140*180/pi;
C2 = 2*140*180/pi;
states_arr_lin = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta2);
% 50 / 50 weight bias:
figure(1);
W1 = W / 2; W2 = W / 2;
C1 = 2*(0.2*W1 - 0.0000942*(W1^2))*180/pi; % lbs/rad
C2 = 2*(0.2*W2 - 0.0000942*(W2^2))*180/pi; % lbs/rad
states_arr_50_50 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta2);
plot(t, states_arr_lin(2,:), '--', 'linewidth', 2);
legends_50_50{end+1} = ['Yaw rate @' num2str(u*ftps2mph) ' mph with linear tires'];
plot(t, states_arr_50_50(2,:), 'linewidth', 2);
legends_50_50{end+1} = [num2str(u*ftps2mph) ' mph with non-linear tires and 50-50 wb'];
K_understeer_50_50 = -m*(x1*C1 + x2*C2)/(C1*C2*l2);
u_char_50_50 = sqrt(l2/K_understeer_50_50)*ftps2mph;
% 60 / 40 weight bias:
figure(2);
W1 = 0.6*W; W2 = 0.4*W;
C1 = 2*(0.2*W1 - 0.0000942*(W1^2))*180/pi; % lbs/rad
C2 = 2*(0.2*W2 - 0.0000942*(W2^2))*180/pi; % lbs/rad
states_arr_60_40 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta2);
plot(t, states_arr_lin(2,:), '--', 'linewidth', 2);
legends_60_40{end+1} = [num2str(u*ftps2mph) ' mph with linear tires'];
plot(t, states_arr_60_40(2,:), 'linewidth', 2);
legends_60_40{end+1} = [num2str(u*ftps2mph) ' mph with non-linear and 60-40 wb'];
K_understeer_60_40 = -m*(x1*C1 + x2*C2)/(C1*C2*l2);
u_char_60_40 = sqrt(l2/K_understeer_60_40)*ftps2mph;
% 40 / 60 weight bias:
figure(3);
W1 = 0.4*W; W2 = 0.6*W;
C1 = 2*(0.2*W1 - 0.0000942*(W1^2))*180/pi; % lbs/rad
C2 = 2*(0.2*W2 - 0.0000942*(W2^2))*180/pi; % lbs/rad
states_arr_40_60 = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta2);
plot(t, states_arr_lin(2,:), '--', 'linewidth', 2);
legends_40_60{end+1} = [num2str(u*ftps2mph) ' mph with linear tires'];
plot(t, states_arr_40_60(2,:), 'linewidth', 2);
legends_40_60{end+1} = [num2str(u*ftps2mph) ' mph with non-linear and 40-60 wb'];
K_understeer_40_60 = -m*(x1*C1 + x2*C2)/(C1*C2*l2);
u_critical_40_60 = sqrt(l2/-K_understeer_40_60)*ftps2mph;
end
figure(1);
legend(legends_50_50{:});
% Add text to plot with understeering coefficient and characteristic speed:
text(4.0, 0.7, ['K_{understeer} = ' num2str(K_understeer_50_50) ' u_{char} = ' num2str(u_char_50_50)], 'FontSize', 16);
title('Yaw rate response for 50/50 weight bias');
xlabel('Time (seconds)');
ylabel('Yaw rate (rad/sec)');
grid on;
hold off;
figure(2);
legend(legends_60_40{:});
% Add text to plot with understeering coefficient and characteristic speed:
text(4.0, 0.7, ['K_{understeer} = ' num2str(K_understeer_60_40) ' u_{char} = ' num2str(u_char_60_40)], 'FontSize', 16);
title('Yaw rate response for 60/40 weight bias');
xlabel('Time (seconds)');
ylabel('Yaw rate (rad/sec)');
grid on;
hold off;
figure(3);
ylim([0, 1.0])
legend(legends_40_60{:});
% Add text to plot with understeering coefficient and critical speed:
text(4.0, 0.8, ['K_{understeer} = ' num2str(K_understeer_40_60) ' u_{critical} = ' num2str(u_critical_40_60)], 'FontSize', 16);
title('Yaw rate response for 40/60 weight bias');
xlabel('Time (seconds)');
ylabel('Yaw rate (rad/sec)');
grid on;
hold off;
% Create a table where the leftmost column is the speed, then understeer coefficient, then characteristic speed:
table = [["50/50 bias", "60/40 bias", "40/60 bias"]', [K_understeer_50_50, K_understeer_60_40, K_understeer_40_60]', [u_char_50_50, u_char_60_40, u_critical_40_60]'];

function states_arr = simulate_bike_2dof(dt, t, m, x1, x2, C1, C2, Iz, u, delta)
% Bicycle model using attack angle conventions:
% Attack angle is the negative of the slip angle
% The sign is embedded in the x1 and x2 distances
A = [
(-C1 - C2)/(m*u), ((-x1*C1 - x2*C2)/(m*u^2)) - 1;
(-x1*C1 - x2*C2)/(Iz), (-(x1^2)*C1 - (x2^2)*C2)/(Iz*u);
];
B = [
(C1)/(m*u);
(x1*C1)/Iz;
];
% Discretize using Euler:
A_dis = eye(2) + dt * A;
B_dis = dt * B;
% Initial conditions:
states = [0; 0];
states_arr = zeros(2,length(t));
% simulation loop:
for i = 1:length(t)
states = A_dis * states + B_dis * delta(i);
states_arr(:, i) = states;
end
end
function delta = slope_it_down(t, dt, at, delta, left_bound, right_bound, slope)
time_to_reach = (right_bound - left_bound) / slope; % time units
delta(1, at/dt:(at + time_to_reach)/dt) = left_bound + slope * (t(at/dt:(at + time_to_reach)/dt) - t(at/dt)); % * sign(right_bound - left_bound);
end

The same Matlab function simulate_bike_2dof was used for this exercise as the weight bias was assumed constant. Figure 5 shows the yaw rate response for the steering input of 3) (the steering angle required to produce a 400 ft radius turn) for different speeds for both the linear and non-linear tires proposed with a 50/50 weight bias; Figure 6 shows the same for a 60/40 configuration and Figure 7 for a 40/60 configuration.

Figure 5: Shows the yaw rate response for different speeds for both the linear tires and the non-linear (quadratic) tires for a 50/50 weight bias configuration. The plot also shows the calculated understeering coefficient and the characteristic speed in the text at the top.

Figure 6: Shows the yaw rate response for different speeds for both the linear tires and the non-linear tires (quadratic) for a 60/40 weight bias configuration. The plot also shows the calculated understeering coefficient and the characteristic speed in the text at the top.

Figure 7: Shows the yaw rate response for different speeds for both the linear tires and the non-linear tires (quadratic) for a 40/60 weight bias configuration. The plot also shows the calculated understeering coefficient and the characteristic speed in the text at the top.

Comparison with 4-5:

For this exercise, the same steering signal input used in 4) and 5) is going to be used to excite the system.

Figure 8: Shows the yaw rate and drift angle time responses for the input generated in 4) for a 50/50 weight bias.

Figure 9: Shows the yaw rate and drift angle time responses for the input generated in 4) for a 60/40 weight bias.

Figure 10: Shows the yaw rate and drift angle time responses for the input generated in 4) for a 60/40 weight bias.

Analysis P1Q6: It can be seen from Figure 5, Figure 6, Figure 7, Figure 8, Figure 9 and Figure 10, that the general pattern is that as speed increases, both the yaw rate and the drift angle tend to increase. Nevertheless, in the cases where the vehicle handling configurations induced understeer (K_understeer > 0.0), this increase tends to have less gain at high speeds, and the time responses of the states tend to have similar final values at speeds greater than the characteristic speed. On the other hand, the vehicle handling configurations that induced oversteer tend to have consistent increasing gains as speed increases as seen in Figure 7 and Figure 10.

50/50 Configuration Analysis:

Figure 5 and Figure 8 show time responses for different steering wheel angle inputs for the 50/50 configuration. It can be seen that the understeer coefficient is about 0.001 which means that the vehicle has tendency towards understeering with a characteristic speed of about 56.7 mph.

The understeering is evident as the gains tend to be lower as speed increases for Figure 5 and Figure 8. Also, notice that in these two figures, at speeds greater than the characteristic speed, the responses start presenting overshoot and oscillations, this is because of the presence of complex conjugate eigenvalues at speeds greater than the characteristic speed.

Overall, the 50/50 configuration presents the most tendency towards neutral steer compared to the other two configurations proposed for this work.

The effect of adding the non-linear tires on this configuration is a decrease in the steady state gain of the yaw rate compared to the linear counterpart. This is due to the fact that the linear tires have a constant slope that always increases with tire load while the non-linear tires have the addition of a squared term that makes the lateral forces decrease after a certain attack angle or load.

60/40 Configuration Analysis:

Figure 6 and Figure 9 show the 60/40 weight bias configuration time responses for the different steering wheel angle inputs. Notice that the understeering coefficient is now much bigger compared to the 50/50 configuration (Ku = 0.005); this is due to the fact that the front is supporting more load, this means that the lateral forces and attack angles will tend to be bigger at the front, making it easier for the front tires to loose grip.

The increased understeering behavior can be appreciated in Figure 6 and Figure 9 both show that the overall steady state gain after the characteristic speed is significantly less compared to the linear tire and the 50/50 configuration.

The effect of adding non-linear tires is a significant decrease in the steady-state gain, even more than the previous configuration.

40/60 Configuration Analysis:

Figure 7 and Figure 10 show the 40/60 weight bias configuration which has a tendency to oversteer given that the understeering coefficient Ku is negative. This system can actually go unstable given that the negative understeering coefficient can produce positive eigenvalues, this happens after the critical speed that for this case is around 42 mph. In both figures, it can be seen that at 40 mph (very close to the critical speed), the system becomes very slow and of very high gain, this is due to the fact that it is very close to becoming unstable. After the critical speed, the time responses tend to infinity.

The effect of adding non-linear tires is a significant increase in the steady state gains of the system given its new tendency to oversteer with this configuration.

7. Comment and interpret your analysis.

- Analysis P1Q1 presents an analysis specific to Part 1 – Question 1.

- Analysis P1Q2 presents an analysis specific to Part 1 – Question 2.

- Analysis P1Q3 presents an analysis specific to Part 1 – Question 3.

- Analysis P1Q4 presents an analysis specific to Part 1 – Question 4.

- Analysis P1Q5 presents an analysis specific to Part 1 – Question 5.

- Analysis P1Q6 presents an analysis specific to Part 1 – Question 6.

Overall takeaways:

1. As speed increases, the steady state gain between steering angle and yaw rate tends to increase. This gain will tend to decrease after the characteristic speed if the vehicle has tendency to understeer, and it will tend to infinity after the critical speed if the vehicle has tendency to oversteer (negative Ku). This is evidenced in Figure 1, Figure 2, Figure 4, Figure 5, Figure 6, Figure 7, Figure 8, Figure 9 and Figure 10.

2. The effect of adding the non-linear tires given by C_i = 2(0.2W_i - 0.0000942 W_i^2)(180 over %pi) lbs/rad is that the lateral force will not always increase with vertical load and/or attack angle as the tire will have a linear region close to zero, but then it will decrease its lateral force, this produces overall lower steady state gains in the yaw rate and drift angle time plots. This is more realistic as it considers non-linearities of the tire behavior that the linear model falls short for operating points far from 0 degrees of attack angle. This can be seen in Figure 5, Figure 6, Figure 7, Figure 8, Figure 9 and Figure 10.

3. Also, it can be seen in the plots when the vehicle tends to understeer that the overshooting and oscillatory behaviors of the yaw rate and drift angle responses tend to increase after the characteristic speed. For the oversteering vehicles, there is no overshoot and no oscillations as the system will not have complex conjugate roots, but it can actually go unstable as seen in Figure 7 and Figure 10.

PART 2: 3-DoF Vehicle (Linear)

Initial setup:

As before, an initial setup Matlab section has to be executed before running the rest of the code for this part. The initial setup code is as follows

%% Load some initial values:
close all;
clear;
clc;
% Conversion factors:
deg2rad = pi / 180;
rad2deg = 180 / pi;
in2ft = 1 / 12;
ft2in = 12;
mph2ftps = 5280 / 3600;
ftps2mph = 3600 / 5280;
% Bicycle model parameters:
W = 3000; % lbs
Ws = 2700; % lbs
g = 32.174; % ft/sec^2
x1 = 3.5; % ft
x2 = -4.5; % ft = -1.0; % ft
h = -1.0; % ft
track_width = 6.0; % ft
Iz = 40000 / g; % lbs*ft^2
Ix = 15000 / g; % lbs*ft^2
c = 0.5; % ft
dl_phi_f = 8000; % lbs*ft
dl_phi_r = 5000; % lbs*ft
dl_dphi_f = 1000; % lbs*ft
dl_dphi_r = 500; % lbs*ft
p = 12*in2ft; % ft
d = 12*in2ft; % ft
gear_ratio = 15; % []
efficiency = 1.0; % Steering gearbox efficiency
Ks = 10*in2ft*rad2deg; % (in*lbs/deg)*(ft/in)*(deg/rad) -> ft*lbs / rad
tm = 3*in2ft; % in*(ft/in)-> ft - Pneumatic trail
% Masses:
m = W / g;
ms = Ws / g;
% u = 30; % ft/sec
C1 = 2*140*180/pi; %*rad2deg; % lbs/deg * (deg/rad) -> lbs / rad
C2 = 2*140*180/pi; % *rad2deg; % lbs/deg * (deg/rad) -> lbs / rad
l2 = x1 - x2; % Wheelbase

1. Repeat the steps in (Part 1: 2-DoF Vehicle) with a three degree of freedom model allowing sprung mass roll. Using the steady-state yaw rate response, construct plots from 0 to 120 mph (i.e. increases of 10 mph) for various speeds without roll steer and with a rear roll steer coefficient of 𝑟 = −0.03.

The steady state gain from steering wheel angle δ to yaw rate r is given by

r over %delta_1 = {u} over {l_2 + u^2 K_{u,%phi}} , where:

l_2 = x_1 - x_2 ,

K_{u,%phi} = K_u + {-C_b m + (C_b (C_{%phi,1} + C_{%phi,2}) - C_a(x_1 C_{%phi,1} + x_2 C_{%phi,2}))({m_s h} over K_%phi)} over {C_1 C_2 (x_1 - x_2)} , and

K_u = {-m (x_1 C_1 + x_2 C_2)} over {C_1 C_2 l_2} .

This steady state gain is calculated for different speeds for a configuration without roll steer and a configuration with a rear roll steer coefficient of -0.03 (ε1=0 and ε2=-0.03) and visualized in the following Matlab code:

%% 1. Repeat the steps in (Part 1: 2-DoF Vehicle) with a three degree of freedom model allowing sprung
% mass roll. Using the steady-state yaw rate response, construct plots from 0 to 120 mph (i.e. 𝛿 ) for
% various speeds without roll steer and with a rear roll steer coefficient of 𝜖𝑟 = −0.03.
% Calculate the steady state gains for different speeds:
speeds = linspace(10, 120, 12)*mph2ftps;
delta2r_w_roll_steer_gain_arr = zeros(1, length(speeds));
delta2r_wout_roll_steer_gain_arr = zeros(1, length(speeds));
dt = 0.01;
t_initial = 0;
t_final = 5;
t = linspace(t_initial, t_final, (t_final - t_initial) / dt);
figure;
hold on;
grid on;
xlabel('Time (seconds)');
ylabel('Gain (𝑟/𝛿)');
xlim([t_initial, t_final]);
ylim([0, 6.0]);
legend_w_roll_steer_arr = cell(1, length(speeds));
legend_wout_roll_steer_arr = cell(1, length(speeds));
for i = 1:length(speeds)
u = speeds(i);
% TODO: Calculate K_understeer
% K_understeer_wout_roll = (-m*(Cb)/(C1*C2*l2));
% K_roll_effect = (ms*h/K_phi)*(Cb*(C_phi1 + C_phi2) - Ca*(x1*C_phi1 + x2*C_phi2))/(C1*C2*l2);
% K_understeer = K_understeer_wout_roll + K_roll_effect;
%
% delta2r_gain_arr(i) = (u) / (l2 + u*u*K_understeer);
% Without roll steer:
eps1 = 0;
eps2 = 0.0;
C_phi1 = C1*eps1; C_phi2 = C2*eps2;
Ca = C1 + C2;
Cb = x1*C1 + x2*C2;
Cc = x1*x1*C1 + x2*x2*C2;
% Roll stiffness:
K_phi = (dl_phi_f + dl_phi_f + ms*g*h); % lb*ft / rad
% Roll damping:
D_phi = (dl_dphi_f + dl_dphi_r); % lb*ft/sec / (rad/sec)
delta2r_wout_roll_steer_gain_arr(i) = (u*C1*(Cb-x1*Ca)) /(Cb*Cb - Ca*Cc + Cb*m*u*u + (x1*Ca*C_phi1 + x2*Ca*C_phi2 - (C_phi1 + C_phi2)*Cb)*(ms*h*u*u / K_phi));
% plot each gain in an xy plot:
subplot(2,1,1);
yline(delta2r_wout_roll_steer_gain_arr(i),'--', ['s.s gain = ' num2str(delta2r_wout_roll_steer_gain_arr(i)) ' @ ' num2str(u*ftps2mph) 'mph'], 'Color', rand(1,3), 'LineWidth', 2);
legend_wout_roll_steer_arr{i} = ['s.s gain = ' num2str(delta2r_wout_roll_steer_gain_arr(i)) ' @ ' num2str(u*ftps2mph) ' mph'];
hold on;
% With rear roll steer coefficient of -0.03:
eps1 = 0;
eps2 = -0.03;
C_phi1 = C1*eps1; C_phi2 = C2*eps2;
Ca = C1 + C2;
Cb = x1*C1 + x2*C2;
Cc = x1*x1*C1 + x2*x2*C2;
% Roll stiffness:
K_phi = (dl_phi_f + dl_phi_f + ms*g*h); % lb*ft / rad
% Roll damping:
D_phi = (dl_dphi_f + dl_dphi_r); % lb*ft/sec / (rad/sec)
delta2r_w_roll_steer_gain_arr(i) = (u*C1*(Cb-x1*Ca)) /(Cb*Cb - Ca*Cc + Cb*m*u*u + (x1*Ca*C_phi1 + x2*Ca*C_phi2 - (C_phi1 + C_phi2)*Cb)*(ms*h*u*u / K_phi));
% plot each gain in an xy plot:
subplot(2,1,2);
yline(delta2r_w_roll_steer_gain_arr(i),'--', ['s.s gain = ' num2str(delta2r_w_roll_steer_gain_arr(i)) ' @ ' num2str(u*ftps2mph) 'mph'], 'Color', rand(1,3), 'LineWidth', 2);
legend_w_roll_steer_arr{i} = ['s.s gain = ' num2str(delta2r_w_roll_steer_gain_arr(i)) ' @ ' num2str(u*ftps2mph) ' mph'];
hold on;
end
subplot(2,1,1);
xlabel('Time (seconds)');
ylabel('Gain []');
title('Steady state gains at different speeds with ε_1=0.0 and ε_2=0.0');
legend(legend_wout_roll_steer_arr{:}, 'Location', 'eastoutside');
subplot(2,1,2);
xlabel('Time (seconds)');
ylabel('Gain []');
title('Steady state gains at different speeds with ε_1=0.0 and ε_2=-0.03');
legend(legend_w_roll_steer_arr{:}, 'Location', 'eastoutside');
hold off;

This code generates the results shown in Figure 11.
Figure 11: Shows the steady state responses for different speeds. The top plot corresponds to a configuration with no roll steer and the bottom one has ε1=0 and ε2=-0.03.

Analysis P2Q1: From Figure 11, it can be observed that adding a negative roll steer at the rear will produce more tendency to understeer on the vehicle as the steady-state gains are going to be lower compared to the configuration with no roll steer. This makes sense as a negative roll steer in the rear will produce less attack angles at the rear, producing less lateral force.

2. Using the 3-DoF equations of motion, simulate the vehicle response to a steering input. Determine the steering input required to result in a 400 𝑓𝑡 radius turn (hint: knowing the forward speed and radius of a circle, the required yaw rate can be calculated). Repeat the result at increments of 10 mph from 10 to 120 mph. Compare the results with the steady-state results from 1) above. As before, we are using this step to validate your simulation model.

The equations of motion for a 3 DOF vehicle with roll and only front steering are:

1. m dot v + m_s (- ddot %phi h) = ({-C_a} over {u}) v + (-C_b over u - mu)r + (C_{%phi,1} + C_{%phi,2}) %phi + C_1 %delta_1

2. I dot r - m_s h c ddot %phi = (-C_b over u ) v + (-C_c over u) r + [x_1 C_{%phi,1} + x_2 C_{%phi,2}] %phi + x_1 C_1
3. I_{x,%phi} ddot %phi - m_s h dot v - m_s h c dot r = m_s h u r - D_%phi dot %phi - K_%phi %phi

These 3 equations can be written in matrix form as

left [ matrix { dot v ## dot r ## ddot %phi} right ] = left [ matrix { m # 0 # -m_s h ## 0 # I_z # -m_s h c ## -m_s h # -m_s h c #I_{x,%phi} } right ]^-1 cdot (left [ matrix { -C_a over u # -C_b over u - mu # 0 # C_{%phi,1}+C_{%phi,2} ## -C_b over u # -C_c over u # 0 # x_1 C_{%phi,1} + C_{%phi,2} ## 0 # m_s h u # -D_%phi # -K_%phi} right ] cdot left [ matrix { dot v ## r ## dot %phi} right ] + left [ matrix {C_1 ## x_2 C_2 ## 0} right ] cdot [%delta]) ;

or in a simpler form:

dot {z}(t) = M^-1 (A cdot z(t) + B cdot %delta(t)) .

The system can be discretized using Euler’s method:

{z}_{k} = z_{k-1} + (dt cdot M^-1 (A z_{k-1} + B u_{k-1})) .